## Slide 1: Computer Networks
A computer network is a collection of computers and computer resources connected together to permit communication between resources
Resources include
  PCs, laptops, servers, mainframes
  Printers
  File servers
  Network broadcast devices
Computer networks permit resource sharing, data sharing, easy communication, e-commerce, telecommuting (also sources of entertainment, etc)
Computer costs: administration and security, cost in lost labor (due to distractions), attacks on the network (denial of service, sabotage/viruses, etc)

## Slide 2: Some Terminology
Host – a compute that can be logged into over network
Local – the computer that the user is on (physically)
Remote – the computer being accessed over the network
Server – a type of computer that offers a service to remote computers on request
Client – the remote computer making requests
Bandwidth – the amount of data that can be transmitted over a unit of time, such as bits per second – indicates to some extent network communication efficiency
Modulation – translating a digital signal to an analog signal (used to send information over analog media like a telephone line)
Demodulation – translating analog back to digital

## Slide 3: Network Hardware
The network itself
  Typically some form of cable
    twisted wire – low bandwidth, old, but cheap
    coaxial
    fiber optic – highest bandwidth, data transmitted as light pulses
  May also utilize wireless, radio, microwave or signals bounced off of satellites in orbit
Broadcast devices
  Used to connect resources together to handle message routing
MODEM
  Modulation/demodulation – devices that permit computers to communicate over an analog medium

## Slide 4: Communicating by Network
Typically, a network consists of multiple nodes
  nodes are different forms of broadcast devices
Switching is used for a message (packet) to be moved from one location to another
  Circuit switched network - pathway between two devices established at the start of communication and remains that way throughout entire communication (telephone network is circuit switched)
  Packet switched network - pathway established as messages is sent from one location to another (most computer networks are packet switched)

## Slide 5: Broadcast Devices
Hub – passes incoming message to all devices connected to it
Switch – uses network address to pass incoming message onto one destination computer
Router – connects multiple networks together, uses destination address to pass message onto the next pathway in the network
Gateway – connects multiple networks of different types together – can translate a message from one protocol to another
A hub (switches,
routers and
gateways will all
have similar
appearances)

## Slide 6: Broadcast Devices
Rack mounted network switches connecting
computers in a local area network
In a hub (upper left), message sent to all devices
In a switch (lower left),
message sent to one destination
In a router, (right) message routed to the proper network switch/hub

## Slide 7: MODEMs and Phone Lines
Before broadband Internet, most home computer users accessed computer networks via a MODEM and their phone lines
  MODEM translates digital signals into tones (analog signal) to be broadcast over the phone lines
Insert telephone handset into
MODEM cradle – computer
connects to MODEM

## Slide 8: Network Topologies
Computer networks can be organized using a variety of layouts
  These topologies describe how computers are connected together
    on the left below, top-down, bus, star, ring, mesh
    on the right, forms of nearest neighbor – 1 D, 2 D, tree, 3D

## Slide 9: Bus Topology
Bus – computers connect via “t” connector to a line that connects all computers
  In essence, the network is one long cable
  Cheap network but not efficient
    if multiple computers attempt to use the bus at the same time, there is a collision and the computers must wait to try again

## Slide 10: Star Topology
All computers connect to a centralized point
  A hub, switch, router or even a dedicated computer used as a “switching point”
  More expensive although does not have to deal with the message contention of the bus (unless the central point becomes a bottleneck)
Two star networks
connected together
with a “crossover”
cable

## Slide 11: Ring Topology
In the ring network, each computer directly connects to two other computers
  A form of nearest neighbor
The network is cheap but the time it takes to communicate with other computers depends on
  The size of the network
  The distance between the two computers in terms of the number of intervening computers
The ring was a direct competitor with the bus network when computer networks were more expensive
  For large networks, the ring is cheap but not very practical

## Slide 12: Mesh Topology
A mesh is also known as a full connected network
Requires point-to-point connections between each device
Not practical for any large network because of the number of connections
  Assume n devices, this requires (n-1)2 connections
  In addition, each device must have n-1 physical ports available to connect to each device
  Mesh networks, if used, are typically used to connect processors together in a parallel processing computer
  Expensive but performance is not impacted by message contention

## Slide 13: Classifying Networks by Size
PAN – personal area network
  found in many households, connects no more than a few devices together
LAN – local area network
  connects computers together in a room or floor of a building, LANs can be combined to create larger LANs
CAN – campus area network
  collection of LANs that make up some organization’s site
MAN – metropolitan area network
  collection of LANs and other forms of connectivity to provide a network within one metropolitan area
WAN – wide area network
  anything larger, the Internet is the largest WAN

## Slide 14: Other Network Classifications
VPN – virtual private network
  Permitting secure off-site access to LAN
  Allows users of network to access network resources remotely
Intranet – local area network that uses IP (Internet Protocol) so LAN supports Internet
Extranet – extending an intranet to permit remote access
  The VPN is a form of extranet that uses encryption technology
Peer-to-peer vs client-server is a model of communication
  Peer-to-peer – no central server, all devices equal
  Client-server – some devices are services, some are clients

## Slide 15: Ethernet
A physical level implementation of a LAN
  Can use either twisted wire or fiber optic cable
  Ethernet repeaters
  48-bit MAC (media access control) addressing
  Error handling mechanisms
  CSMA/CD (see next slide)
Produced by 3Com in 1980
  Originally implemented using the bus topology but also supports the star topology
  Theoretical bandwidth of 10 Mbps made it very popular, today its upper bandwidth is 100 Gbps

## Slide 16: CSMA/CD
Carrier Sense Multiple Access with Collision Detection
  Device senses media for message traffic
  If none found, device places message onto media
  Device continues to sense for message traffic
    if another device uses network, the message over the network would not match the device’s transmitted information, thus a collision is detected
  Upon collision detection, sending device(s) sends out a jam signal to prevent other devices from using network
  Device(s) wait a random amount of time before trying again

## Slide 17: Network Protocols
A protocol is a set of rules to govern how people behave and interact
  This might be diplomacy, etiquette, means of communication
A network protocol is a set of rules that govern how messages can be converted from their application software form to a form that can be transmitted over network
  And mapped back from the messages received over network to a message for an application
A protocol can include
  Forms of addressing
  Size of messages (packets)
  Error handling mechanisms and encryption

## Slide 18: OSI Model
The Open Systems Interconnection model was generated to provide network developers with a target
  OSI is not any particular protocol, but it describes what all network protocols should include
  An implementer of a network is free to add mechanisms to the OSI model but should try to fit the model
  The OSI model consists of 7 layers
  Existing networks have numerous implementations for the 7 layers
TCP/IP (which we examine later) is an older model that has some overlap with OSI, but OSI being newer has ideas that are not found in TCP/IP

## Slide 19: 7 Layers at a Glance
Layers 7-5 operate at the message level
  That is, treating the message as a whole
Layer 4 breaks messages into “segments” such as packets
Layers 3-1 operate at the network layer
Layer 1 involves the physical network

## Slide 20: Layers 7-5
Layer 7: Application layer
  From the application software, a message is created
    telnet, ftp, email, http all operate at this level
Layer 6: Presentation layer
  Translate message into a common syntax such as stripping out the hierarchical notation of XML or removing special characters such as \0 in C programs
  Encryption, if used, is applied here
    SSL, TLS, MIME among others implement layer 6
Layer 5: Session layer
  Maintains session between two devices
    NetBIOS, SAP, PPTP, SOCKS

## Slide 21: Layer 4: Transport Layer
Divide message into segments
Implement reliability by error correction
  for instance, through a checksum
  stamp each segment, for instance, 4 of 7
Implement control flow
  if two devices communicate at different rates (speeds), handle it here
Many implementations including
  tcp, udp, sctp

## Slide 22: Layer 3: Network Layer
Addressing takes place here
Messages at this level are variable length
  add or utilize host and destination addresses here such as IP addresses
  messages are further broken into packets
  a message might consist of a single packet or hundreds depending upon the length of the message
If segments from layer 4 are not already packets, packets are formed here
  IP, AppletTalk, IPX, ICMP, ARP
Routers operate at layer 3

## Slide 23: Layer 2: Data Link Layer
Messages on the same network are transmitted at this layer
  they do not need to involve layer 3
Packets are broken into frames for synchronization (start bits)
Two sublayers
  logical link control sublayer for multiplexing
  media access control sublayer to use MAC addresses
Many implementations including
  IEEE 802.2, IEEE 802.3, PPP, X-25, ATM
  switches operate at this layer

## Slide 24: Layer 1: Physical Layer
How devices communicate over the media
Includes details of voltage, modulation/demodulation
How to establish and terminate connections, how to detect message traffic and resolve it
  IEE 802.3, IEEE 802.11, Bluetooth, USB, hubs
Packets are placed on the media for transmission at this layer (or received from the media)
Ethernet is implemented at both layers 1 and 2

## Slide 25: OSI Mapping
Notice how
headers are
affixed at each
layer except
for layer 1

## Slide 26: TCP/IP
TCP/IP is known as a protocol stack
  Although TCP and IP are protocols themselves, there are other protocols that can operate in conjunction with them
  TCP and IP were developed separately but united to help develop the Internet
  TCP handles the higher layers and IP handles the lower layers
TCP/IP has 4 layers
  These 4 map roughly onto the 7 layers of OSI with some missing components

## Slide 27: TCP
Application layer: similar to OSI’s layers 7-6
  Messages are taken from applications
  Handles different communication protocols such as ftp, smtp, http
    libraries are available to handle the different types of protocols
Transport layer: similar to OSI’s layer 4
  Two forms of data streams, TCP and UDP (see next slide)
  This layer has mechanisms to maintain a session with the remote computer, similar to OSI’s layer 5

## Slide 28: TCP vs UDP
Two forms of data packets
  Transmission control protocol
    uses sequence numbering (e.g., 4 of 7)
    contains acknowledgement information for network handshaking and control flags
  User datagram protocol
    foregoes reliability information making the packets more concise
UDP is used primarily when guaranteed delivery is less important than speed
  For instance, TCP will be used for email and web pages while UDP will be used for streaming audio and video and for DNS and DHCP

## Slide 29: Comparing the Packets
TCP
UDP

## Slide 30: IP
Internet layer: similar to OSI’s layer 3
  Responsible for sending packets from one network to another
    routers operate at this level
  Addressing takes place here using IP addresses
    IPv4 – 32 bits (4 octets of 8 bits each, or 4 numbers from 0-255) such as 127.31.49.6, provides 232 different addresses (over 4 billion) but not all addresses are used leading to a situation where we have run out of addresses!
    IPv6 – 128 bits (64 bit network address for routing, 64 bit interface number), provides 2128 different addresses
Link layer: similar to OSI’s layers 1 & 2
  Performs all services related to the physical network
    hubs, switches and the physical network operate at this level

## Slide 31: IPv4 Network Classes
This is a way to assign IP addresses based on class
  Class A network has millions of individual addresses
  Class C networks have 256 individual addresses but there are millions of class C networks
Although obsolete today, network classes still exist

## Slide 32: TCP/IP Mapping

## Slide 33: TCP/IP Handshaking
A network handshake involves
  Source computer requesting communication with destination computer
  Destination computer acknowledging
In TCP/IP, there is a three-way handshake
  Machine 1 sends synchronization packet (SYN)
  Machine 2 replies with synchronization and acknowledgement packet (SYN/ACK)
  Machine 1 confirms with acknowledgement (ACK)
    examine the TCP packet (slide 36), there is an entry for acknowledgement number to support the TCP/IP handshake

## Slide 34: TCP/IP Ports
Aside from IP addresses, messages are sent using a port address
  The address is used to specify the type of message
  This in turn specifies how the message is expected to be handled
    in terms of application software or server
Most software have officially designated port addresses
  This helps with security
    ftp (20), ssh (22), telnet (23), smpt (25), http (80, 8080), https (431)

## Slide 35: Network Address Translation
Converting external IP address to internal IP address
  Basic NAT – one-to-one mapping, hides internal IP addresses, also used when two networks have incompatible addresses
  Many-to-one – used so that a single external IP address can be converted into many internal addresses
    when organizations have fewer IP addresses available than devices
    provides anonymity in that internal addresses are “hidden”
    also called IP Masquerading or NAT overload
  NAT requires converting message header (which then requires computing a new checksum)

## Slide 36: Network Software
Telnet/ssh – log in to remote computer
  Need an account
  telnet not secure, ssh is by using encryption
R-utilities like rlogin – for a network of Unix computers that share authentication so that you don’t have to log in
Ping – send packets to remote machine – used to determine if remote machine is accessible and to gage efficiency of network
Traceroute – like ping, but respond with addresses of all intervening network nodes reached (usually routers)
HTTP – the hypertext transfer protocol, basis for web browser communication
FTP – file transfer protocol, older form of transferring files prior to HTTP
  anonymous logins available to permit access to public ftp areas

## Slide 37: IP Aliases vs IP Addresses
Because IP addresses are hard to remember
  We tend to use IP aliases for http, ftp, ssh, etc
Routers use IP addresses
  We need a way to map from aliases to addresses
  We use the domain name system for this
    DNS servers are available on the Internet to perform the mapping
    a local DNS server will know enough to contact other DNS servers to obtain proper mapping
Programs that perform mapping include
  nslookup, host, dig

## Slide 38: Linux Network Handling
Start the network service
  /sbin/service network start (or restart)
Obtain IP address and routing table information
  Done when the service starts
  You can view this information using the ip program (newer), or ifconfig and route programs (older)
Important Linux network files
  /etc/hosts – IP alias to address mapping for commonly accessed machines (allows you to skip DNS step)
  /etc/resolv.conf – location of your local DNS servers
  /etc/sysconfig/network-scripts – location of network information and scripts
  /etc/hosts.allow and /etc/hosts.deny – IP addresses of computers allowed or disallowed access

## Slide 39: Network Security
Firewall
  A program that contains a set of rules
  Incoming (and outgoing) messages are examined against the rules to be permitted in (out) or rejected
  Rules might test type of message (protocol), destination port, source IP address
Antiviral software
  Attempts to identify if a file has a virus (often done by comparing file’s size to checksum data)
  Also can look for other forms of malware (spyware)
Network intrusion detection software
  Look for evidence of illegal access into computer or reconnaissance attacks

## Slide 40: Types of Network Attacks
Denial of service
  Flood a server with requests so that it cannot handle all of the requests
IP spoofing
  Use someone else’s IP address to intercept messages
ARP poisoning
  Modify a switch’s address table so that message intended for one machine go elsewhere
Buffer overflow
  Overflow an area of memory to insert your own instructions to be executed
SQL injection
  Send your own database instructions to a backend database to obtain, alter or destroy data stored there
    we will examine attacks again in chapter 15

## Slide 41: Morris’ Internet Worm
Cornell Graduate student Robert Morris
Wrote a program to exploit weaknesses in Unix
Launched on November 2, 1988, it infiltrated about 6000 Unix machines during a 3 day period
  Enter Unix systems by guessing weak passwords, exploiting weaknesses in sendmail and finger (using buffer overflow among other techniques)
  Once logged in, it uploads the rest of itself to spawn copies to other networked computers using r-utilities
Morris claims the attack was not malicious but to prove the security holes in Unix

## Slide 42: The Internet
Based on three technologies
  Packet switching – messages are routed while making their way across the Internet
  Routers – devices that perform the packet switching, moving messages from one network to another
  IP addresses – the method by which we address our messages, along with DNS servers to map aliases to addresses
Users use application to send out machine (e.g., http request)
  Computer packages up the message into packets
  Request to DNS server to translate destination IP alias into IP address until address properly mapped
  Given IP address from DNS server, IP address added to message
  Local router sends packets out onto your local area network to Internet point of presence (a gateway)

## Slide 43: Continued
Each packet is sent out on Internet
  Packets are transmitted from one site to another
  At each site, the router routes the packet to another let of the network
  Multiple packets of the same message will find their own paths (quite possibly different paths)
At the destination site, received packet sent to proper internal LAN via internal routers
  NAT may be required
  At proper LAN, network switch broadcasts message to destination computer
  If multiple packets expected (e.g., packet 3 of 5). destination computer waits for all packets to arrive
  Puts message together for appropriate application software
  When full message arrives (if correct), destination sends acknowledgement (or request for missing or erroneous packets)

## Slide 44: Subnet Masks
Router needs network address portion of an IP address
  AND netmask to destination IP address
Assume IP address of 10.11.241.105 and class C network (first 24 bits are network address, last 8 bits are machine address)
  Netmask for network address is 255.255.255.0
  Netmask for machine address is 0.0.0.255
    recall 255 = 11111111 in binary, 0 = 00000000
  Example

## Slide 45: Example
To obtain network address:
    10.11.241.105
    AND 255.255.255.0
    = 10.11.241.0
    00001010.00001011.11110001.01101001
    11111111.11111111.11111111.00000000
    = 00001010.00001011.11110001.00000000
To obtain machine’s address
    00001010.00001011.11110001.01101001
    AND 00000000.00000000.00000000.11111111
    = 00000000 . 00000000 . 00000000 .01101001
    = 0.0.0.105

## Slide 46: The Internet vs the World Wide Web
People often confuse the two
  The Internet is the physical infrastructure (media, routers) along with the computers
  The web are the collection of documents, linked together by hyperlinks, that are stored on some specific computers on the Internet
    the web sits on top of the Internet
    without the Internet, we would not have the WWW
You may have heard people say things like
  “I’ve lost the Internet” or “The Internet is down”
  They have lost their connection only
    This might be a hardware failure, a software failure, a problem with their firewall, lost connection with their DNS server
  In fact, the Internet was built to survive a nuclear war!

## Slide 47: History of the Internet
1968 – four research organizations (funded by the department of defense) form a computer network for long-distance communication
  The ARPAnet, at University of Utah, UCLA, UC Santa Barbara, Stanford Research Institute
  Uses packet switching, allows remote access to computers on other sites and transfer of files, first message sent October 29, 1969
June 1970 – 9 computers connected
September 1971 – 18 computers
1972 – 29 computers
1973 – 40 computers
1971 – first email
1973 – FTP implemented
1973 – two satellites in use, connects computers in Hawaii and Norway

## Slide 48: Continued
1974 – UK adds X.25 protocol
1975 – 57 computers
1979 – Duke students create UUCP (electronic bulletin boards) – eventually becomes Usenet
1983 – military portion of ARPAnet separated to form MILNet, TCP/IP used, network renamed Internet
In the 1980s, push to connect US universities (edu) and libraries to Internet, home computer users gain access through pay sites
  Computer hosts grow to tens of thousands

## Slide 49: Continued
1990s
  First web browser, MOSAIC, created (1994), creating the WWW
  US Legislature allows companies to become Internet service providers
  Operating systems (like Windows 95) supports Internet access
  Users of the Internet grows from thousands to millions and beyond
2000s
  Smart phone and tablet access
  Billions of Internet users
  Trillions of web documents (exact number is not known)

## Slide 50: Internet Users

## Slide 51: Internet Issues
Who controls the Internet?
  In the 90s, US government handed control to commercial companies and organizations like
    ICANN – Internet Corporation for Assigned Names and Numbers
    WWWC (W3C) – World Wide Web Consortium for standards on web site construction (html, css, xml, etc)
  Governments enact legislature on Internet usage
    copyright infringement, anti-piracy, obscenity laws, censorship
We have reached many limitations of the Internet
  Running out of IPv4 addresses, Internet backbone not developed to support billions of users and streaming audio/video
Last mile technology still in use
  Many users still use the telephone lines which limit their bandwidth, broadband access not available in rural areas, third world countries, etc
  Cell phone technology used in some cases but 3G has many problems, 4G not yet available everywhere

## Slide 52: Semantic Web
The WWW has limitations – poorly indexed info, flat files
Add artificial intelligence capabilities to improve web access
  Searching and inferencing to permit websites to solve problems for you
  Creating of representative-bots to act on your behalf
Construction of the semantic web is ongoing, started around 2001
  Requires converting information into ontologies, better query languages
  Creation of intelligent agents – bots (software) that can make inferences, each agent has a specific, small role to play, groups of bots work together to solve the problem
Semantic web is in its infancy but currently being used to support
  Intelligence gathering in support of antiterrorism
  Medical research

## Slide 53: Cloud Computing
Already here but we look to improve it
A network of resources made available remotely
  Remote storage
  Remote processing
Somewhat like 3rd generation computers, you access the mainframe from your office using a dumb terminal
Here, you access the cloud remotely through your (possibly mobile) I/O device(s)
  Most or all computing and storage are located elsewhere