## Slide 1: Evolution of the Intel Architecture
8086 released in 1978, ranged between 4-10 MHz
  16 bit architecture which grew out of the earlier 8008 and 8080 architectures
    mostly backward compatible with 8008, 8080 and 8085
  20-bit address space by
    left shifting segment register 4 bits to be a 20-bit base and adding index register as an offset
  integer only, signed and unsigned
    microcoded multiply and divide operations
  CPU had 40 pins whose uses overlapped based on clock cycle
    see next slide
    pins and address/data bus are multiplexed (address during first cycle, data during second – fourth cycles)
  floating point available by adding 8087 coprocessor

## Slide 3
Notes:
3: add base address
and offset
5: 4-item instruction
buffer (not for
prefetching but
because instruction
lengths vary)
10: address bus
11 & 12: data and
control buses

## Slide 4: Addressing Modes and Execution Time
Each mode is listed as two numbers
  1st for mov instruction, 2nd for ALU
Register-register: 2, 3
Register-immediate: 4, 4
Register-memory: 8+EA, 9+EA
Memory-register: 9+EA, 16+EA
Memory-immediate: 10+EA, 17+EA
  EA = time to compute effective address which ranges from 5 to 12 cycles
  multiply ranged from 70-160, divide from 80-190
For jump instructions: 11 (unconditional, no label), 15 (unconditional, labeled), 16 (conditional, labeled)

## Slide 5: 80286
Introduced in 1982
  address and data bus and pins separated (no longer multiplexed)
  protection capabilities to detect memory violations
    two modes: real mode and protected mode (used to permit access to larger memory spaces, up to 4GB)
    this is because the 286 was designed for multiuser and multitasking systems (even though MS DOS and early versions of Windows were not)
  ranged from 4-25 MHz
    performance averaged CPI of about 5
  still required a math coprocessor for FP (80287)

## Slide 7: 80386
Released in 1985
Extended the 286 architecture to 32 bits
  all registers retained but “E” versions added to add the extra 16 bits
Third mode added (virtual mode multitasking)
  added paging translation unit for virtual memory address translation
Added several new built-in data types: char, string, long int, boolean, pointer
  still required math coprocessor for FP
  Clock rates ranged from 12 MHz to 40 MHz

## Slide 9: 486 Processor
Added a pipeline (see next 2 slides)
Added floating point functional unit
  no longer needed the math coprocessor
  FP unit has its own bus to connect to FP registers
  functional unit provided a degree of parallel processing in that while FP operations were executed, the pipeline would continue to fetch and execute integer operations
Added an atomic operation to better implement synchronization
Contained 8KB combined instruction/data cache
  later expanded to 16KB
Clock rates range from 33 MHz to 100 MHz

## Slide 10
The 486 Pipeline
5 stages
  Fetch 16 bytes worth of instruction
    may be 1 instruction, part of 1 instruction, multiple instructions
  Decode stage 1 – examine 16 bytes to identify whole instruction
    if buffer does not contain entire instruction, stall pipeline and continue fetching instruction
    divide 16 bytes into instruction(s) (find the end of each instruction)
  Decode stage 2 – decode the next instruction
    includes fetching operands from registers
  Execution – ALU operations, branch operations, cache (mov) instructions
    may take multiple cycles if ALU operation requires multiple cycles (*, /, FP) or requires 1 (or more) memory accesses
    further stalls needed if memory access is a cache miss
  Write result of load or ALU operation to register

## Slide 11
486 Difficulties
Stalls arise for numerous reasons
  17 byte long instructions require 2 instruction fetch stages
  ALU memory-register/memory-immediate takes at least 1 additional cycle
    possibly two if memory item is both source and destination
    such a situation stalls instructions in the decode 2 stage
    or if there is a cache miss
  Complex addressing modes can cause stalls
    pointer accessing (indirect addressing) takes 2 memory accesses
    scaled addressing mode involves both a shift and an add
    again, stalls occur in the decode 2 stage
  Branch instructions have a 3 cycle penalty
    branches are computed in the EX stage (4th stage)
    some loop operations take more than 1 cycle to compute adding a further stall

## Slide 12
486 Examples
Example 1:
  three data movements, no stalls
Example 2:
  data hazard, 1 cycle of stall
Example 3:
  branch penalty

## Slide 13: 486 Overall Architecture

## Slide 14: Pentium Architecture
Summarizing problems with the 486 pipeline
  variable length instructions, variable complexity of operations, memory-register ALU operations, indirect addressing
  to improve performance using RISC features, Pentium (586) architects needed to rethink things while still implementing backward compatibility
CISC architectures handle the fetch-execute cycle through a microprogrammed control unit
  a microprogram consists of a sequence of microinstructions, each being of equal length and taking 1 clock cycle (usually) to execute
Re-implement the pipeline as follows
  continue to use an instruction fetch unit to fill a buffer with instructions
  use a separate decode unit to identify each instruction and decode it into microcode
  issue microinstructions to a pipeline

## Slide 15: Control and Micro-Operations
An example architecture is shown to the right
Each of the various connections is controlled by a particular control signal
  MBR to the AC controlled with signal C11
  PC to MAR by C2
  AC to ALU C7
    note that this figure is incomplete
A microprogram is a sequence of micro-operations
this is not an x86 architecture!

## Slide 16: Example
Consider a CISC instruction such as Add R1, X
  X copied into MAR and a memory read signaled
  datum returned across data bus to MBR
  adder sent values in R1 and MBR, adding the two, storing result back into R1
This sequence can be written in terms of micro-operations as:
  t1: MAR  (IR (address) )
  t2: MBR  Memory
  t3: R1  (R1) + (MBR)
  t3: Acc  (R1) + (MBR)
  t4: R1  (Acc)
Each micro-operation is handled by one or more control signals
  For instance, MBR  Memory is C5
t1 – t5 are clock cycles, each
microinstruction executes in
separate clock cycles

## Slide 17
Control Memory
...
Jump to Indirect or Execute
...
Jump to Execute
...
Jump to Fetch
Jump to Op code routine
...
Jump to Fetch or Interrupt
...
Jump to Fetch or Interrupt
Fetch cycle routine
Indirect Cycle routine
Interrupt cycle routine
Execute cycle begin
AND routine
ADD routine
Each micro-program consists of one or more micro-instructions, each stored in a separate entry of the control memory
The control memory itself is firmware, a program stored in ROM, that is placed inside of the control unit
Note: each micro-program ends with a branch to the
Fetch, Interrupt, Indirect or Execute micro-program

## Slide 18: Example of Three Micro-Programs
Fetch: t1: MAR  (PC) C2 t2: MBR  Memory C0, C5, CR PC  (PC) + 1 C* t3: IR  (MBR) C4
Indirect: t1: MAR  (IR (address) ) C8 t2: MBR  Memory C0, C5, CR t3: IR(address)  (MBR (address) ) C4
Interrupt: t1: MBR  (PC) C1 t2: MAR  save address C* PC  routine address C* t3: Memory  (MBR) C12, CW
  CR – Read control to system bus
  CW – write control to system bus
    C0 – C12 refers to the previous figure
    C* are signals not shown in the figure

## Slide 19: Horizontal vs. Vertical Micro-Instructions
Micro-instruction Address
Function Codes
Jump
Condition
Internal CPU Control Signals
Micro-instruction Address
Jump Condition
System Bus
Control Signals
Horizontal micro-instructions contain 1 bit for every control signal controlled by the control unit
Vertical micro-instructions
use function codes that
need additional decoding
This micro-instruction requires 1 bit for every control line, it is longer than the vertical micro-instruction and therefore takes more space to store, but does not require additional time to decode by the control unit
Micro-instruction address points to a branch in the control memory and is taken if the condition bit is true

## Slide 20: Micro-programmed Control Unit

## Slide 21: Continued
Decoder analyzes IR
  delivers starting address of op code’s micro-program in control store
    address placed in the to a micro-program counter (here, called a Control Address Register)
Loop on the following
  sequencer signals read of control memory using address in microPC
  item in control memory moved to control buffer register
  contents of control buffer register generate control signals and next address information
    if the micro-instructions are vertical, decoding is required here
  sequencer moves next address to control address register
    next instruction (add 1 to current)
    jump to new part of this microprogram
    jump to new machine routine

## Slide 22: Pentium Architectures
Pentium I released 1993
  upgraded to 64-bit data bus
  superscalar 5-stage pipeline (2 parallel pipelines)
  branch speculation added
  separate instruction and data catches
  FP portion of the processor had an infamous bug requiring the entire CPU be replaced!
Pentium II released 1995
  added L2 cache
Pentium III released 1999
  both PII and PIII used 14-stage pipelines
Pentium IV released 2000
  superscalar expanded to 3 parallel pipelines
  21-31 stage pipeline

## Slide 23: Pentium IV: RISC features
RISC features implemented on microinstructions
  instead of machine instructions
Microinstruction-level pipeline
Dynamically scheduled micro-operations
Reservation stations (128)
Multiple functional units (7)
Branch speculation via branch target buffer
  speculation at micro-instruction level
    instead of an ROB, decisions made at the reservation stations
    miss-speculation causes reservation stations to flush their contents
    correct speculation causes reservation stations to forward results to registers/store units
  trace cache used (discussed shortly)

## Slide 24: Pentium II-III Pipeline
IF unit: 3 stages
ID unit: 2 stages
Issue unit: 2 stages
  up to 3 microinstructions issued per cycle
  register renaming occurs here
  instructions sent to reservation station
Execution units: 1-32 stages
  1 for int, up to 32 for FP
Write back: 3 stages
Commit: 3 stages
  up to 3 microinstructions can commit in any cycle

## Slide 25: Pentium IV Overall Architecture

## Slide 26: Specifications
7 functional units:
  2 simple ALUs (add, compare, shift) – ½ cycle execution to accommodate up to 2 micro-operations per cycle
  1 complex ALU (integer multiplication and division) – multicycle, pipelined
  1 load unit and 1 store unit – including address computation
  1 FP move (register to register move and convert)
  1 FP arithmetic unit (+, -, *, /) – multicycle, pipelined, some SIMD execution permitted on these units
128 registers for renaming
  reservation stations are used rather than a re-order buffer
  instructions must wait in reservation stations longer than in Tomasulo’s version, waiting for speculation results

## Slide 27: Trace Cache
Instruction cache
  caches blocks of instructions recently executed together
Trace cache encodes branch behavior implicitly
Miss-speculated instructions would be discarded from the cache
  stores microinstructions (not machine instructions)
Combining a trace cache and branch target buffer minimizes microinstruction fetch and decoding
  as long as the microinstructions remain in the trace cache
Miss-predictions at the
microinstruction level are
far rarer than miss-predictions
at the machine level

## Slide 28: Source of Stalls
Process breaks down as follows
  in the issue stage
    branch miss-predictions
    cache misses, particularly trace cache miss
    reservation stations full
    limited number of entries in the commit buffer
    less than 3 instructions fetched in 1 cycle
    less than 3 microinstructions can be issued at the time
  at the commit stage
    branch miss-predictions
    instructions not ready to commit yet
    branch computation not yet available

## Slide 29: Continued
Miss-prediction of microinstruction are very infrequent (about .8% for int, .1% for FP)
  FP are often more predictable because they involve a lot of for loops
  machine language level miss-speculation between .1% and 1.5%
Trace cache has nearly a 0% miss rate
  L1 and L2 data caches have miss rates of around 6% and .5% respectively
  machine’s effective CPI ranges from around 1.2 to 5.85 with an average of around 2.2
    machine instructions, not micro-operations

## Slide 30: Intel Core (iCore)
Multi-core processors (started with 2 cores)
  originally released with two cores where one was disabled
Same basic architecture as Pentium III but with lower clock rates, this was offset by several new innovations
  issue up to 4 microinstructions at a time
  more efficient decode stages
    using macro-ops which attempts to combine two micro-instructions into a single one such as a compare and conditional branch
  more efficient execution units
    one cycle throughput due to pipelined ALU units (previously had a 2-cycle throughput)
  larger caches and buses
  no SMT processing (developed for Pentium IV)
  lower power consumption (needed when there are multiple cores)
  iCore has released processors of 1, 2, 4 and 6 cores

## Slide 31: Intel Core i7
Aggressive out of order speculation
  pipeline reduced from 31 to 14 stages
Instruction fetch unit
  retrieves 16 bytes to decode
    feeds a queue that can store up to 18 instructions at a time
  multilevel branch target buffer, return address stack for speculation
    miss-predictions cause a penalty of about 15 cycles
  32 KB instruction cache
  if a loop is detected that contains fewer than 28 instructions or 256 bytes
    these instructions will remain in a buffer to repeatedly be issued (rather than repeated instruction fetches)

## Slide 32: Continued
Decoding converts machine instructions into microcode using any of four decoders
  simple micro-operation instructions (2 each)
  complex micro-operation instructions (2 each)
Instruction issue can issue up to 6 micro-operations per cycle to
  36 centralized reservation stations
  6 functional units including 1 load and 2 store units that share a memory buffer connected to 3 different data caches

## Slide 33: i7 Architecture

## Slide 34: i7 Performance
CPI for various SPEC06
benchmarks
Average CPI is 1.06 for
integer programs
and .89 for FP (machine
instructions, not
micro-instructions)
i7 susceptible to miss-speculation resulting in “wasted” work
Up to 40% of the total work that goes into Spec 06 benchmarks is wasted
Waste also arises from cache misses (10 cycles or more lost with an L1 miss, 30-40
for L2 misses and as much as 135 for L3 misses)

## Slide 35: Multicore Processors
Each core is a separate processor with its own registers, ALU, control unit, local bus, and L1 cache
  L2 cache is shared among all cores
  L3 off chip may be added
  performance of multicore processors shown below
    speedup is close to but not always linear to the number of cores

## Slide 36: A Balancing Act
Improving one aspect of our processor does not necessarily improve performance
  it might actually harm performance
    lengthening pipeline depth, increasing clock speed in the P4 without adding reservation stations or using a trace cache degrades performance
    stalls arise at issue stage due to needing more instructions to issue
    cache misses have greater impact when the clock speed is increased
    without accurate branch prediction and speculation hardware, stalls from miss-predicted branches can have a tremendous impact on performance
    we saw this in both the ARM and i7 processors

## Slide 37: Continued
As clock speeds increase
  stalls from cache misses create a bigger impact on CPI
  larger caches and cache optimization techniques are needed
To support multiple issue of instructions
  need larger cache-to-processor bandwidth
Increasing instruction issue rate
  requires a proportional increase in the number of reservation stations and reorder buffer size